## Slide 1: PIMID: A Full-System Simulator for Processing-in-Memory with Intricacy and Diversity
Yuan He1, Masaaki Kondo1, Galen M. Shipman2,
Jered B. Dominguez-Trujillo2, and Kazi Asifuzzaman3
1R-CCS, 2LANL, 3ORNL

## Slide 2: Next Generation High Performance Architecture Research Team RIKEN Center for Computational Science
FugakuNEXT

## Slide 3: Outline
Introduction and motivation
  Challenges in current PIM research tools
PIMID: our solution
Key features of PIMID
Comparison with existing Tools
Conclusions and future considerations

## Slide 4: The Memory Wall Challenge
Growing Computational Demands
  Conventional memory systems struggle to keep pace
  Data movement costs dominate energy consumption
  Need innovative approaches to reduce data movement
Processing-in-Memory (PIM) promises to
  Integrate computation closer to the memory system
  Reduce data movement between processor and memory
  Improve performance and energy efficiency
But current PIM research tools have significant limitations...

## Slide 5: Challenges in Current PIM Research Tools
Scope Limitations
  Mostly device-centric
  Limited full-system perspective
Technology Support
  Mostly DRAM-centric
  Missing SRAM, STT-MRAM, and other emerging memory technologies
Limited flexibility in architectural modeling
  Assuming naive PE placements and addressing
  Lacking network models for in-memory communication
  Missing proper programming model support
  Missing power models for compute parts

## Slide 6: Our Solution => PIMID*
A comprehensive full-system PIM simulator built on proven foundations
  Extended from MultiPIM
    https://github.com/Systems-ShiftLab/MultiPIM
  MultiPIM itself is already a somehow mature simulator allowing architectural exploration on PIM
  We exetended it with new capabilities
Key features to add
  Co-simulation of host and PIM devices
  Multiple memory technologies support
  Finer-grained configurability
  Network model within the memory system
  Power Model for compute
*PIMID = Processing-in-Memory with Intricacy and Diversity
CPU
MC

## Slide 7: Key Feature 1: Host-Device Co-Simulation
Two MultiPIM processes co-simulate at the same time
They communicate through sockets to mimic interactions between host and devices
This enables one run to collect simulation results of the entire system

## Slide 8: Key Feature 2: Multiple Memory Technologies
Current MultiPIM supports DRAM (DDR/HBM) through two extra tools
  Timing from Ramulator
  Power from DRAMPower
PIMID has added timing/power support for
  SRAM through CACTI
  STT-RAM from NVSIM
An interesting outcome after this would be to allow users to have simulated systems having devices from multiple memory technologies

## Slide 9: Key Feature 3: Fine-Grained PE Placements
PEs in MultiPIM are assumed to have a unified memory address space with the host so PEs can only be seen as rank-level components
  Communication between PEs could only happen through the host memory controller
By allowing the placements of PEs inside memory chips and banks, we need to have Discrete addressing for subarray-/bank-/chip-wide PEs

## Slide 10: Key Feature 4: Multiple Programming Model Support
Programming model support for multi-processing workloads in MultiPIM is shared memory
  Workloads can be written/compiled with OpenMP and run in MultiPIM
  This is OK if PEs are placed in ranks, a directory can be placed in the host MC to guarantee cache coherence between PEs
  However, this is not reasonable if PEs are allowed to be placed near the banks or inside the chips => a lot of coherence traffic is about to cross the host MC
So we added message passing as another option
  Workloads can be written/compiled through MPI with PIMID
  Explicit message exchange happens between the PEs
=> A more realistic option here would be to have
  Memory sharing up to chip scale
    OpenMP-based workloads works if offloaded to PEs in the same chip
  Message passing between PEs communicating beyond memory chips

## Slide 11: Key Feature 5: Flexible Network Support
MultiPIM already has booksim to support networking inside the memory
We integrated GARNET to enable comprehensive network modeling
  Topologies
  Routing algorithms
  Flow control
Can see this as a hypothetic feature since current memory designs only have h-trees and crossbars internally

## Slide 12: Key Feature 6: Comprehensive Power Modeling
No power modelling at all for computing parts in MultiPIM
We added McPAT to support power modelling for the host processor and PEs
  From simple in-order to OoO cores with caches

## Slide 13: Comparisons with Existing Tools

## Slide 14: Conclusions
PIMID advances PIM research through
  Comprehensive scope - host-device co-simulation
  Technology diversity - DRAM, SRAM, STT-MRAM support
  Architectural flexibility - Fine-grained PE placement with multiple addressing modes
  Programming model for MP workloads - OpenMP + MPI support
  Detailed networking - GARNET-based interconnects
  Complete power modeling - Host, PE, and memory power

## Slide 15: Future Work
Immediate plan
  Open-source release => Community access and contributions
Scheduled updates
  Continued bug fixes and support
  Hardware validation - validation support with FPGA?
  Upgrade to Intel PIN 3