## Slide 1: PIMID: A Full-System Simulator with Intricacy and Diversity for Processing-in-Memory
Yuan He*, Masaaki Kondo*, Galen M. Shipman^,
Jered B. Dominguez-Trujillo^, and Kazi Asifuzzaman+
*R-CCS, ^LANL, +ORNL

## Slide 2: Outline
Introduction and motivation
  Challenges in current PIM research tools
PIMID: our solution
Key features of PIMID
Sample simulation results
Comparison with existing Tools
Conclusions

## Slide 3: The Memory Wall Challenge
Growing computational demands but…
  Conventional memory systems struggle to keep pace
  Data movement costs dominate energy consumption
  Need innovative approaches to reduce data movement
Processing-in-Memory (PIM) promises to
  Integrate computation closer to the memory system
  Reduce data movement between computing and memory
  Improve performance and energy efficiency
But current PIM research tools have significant limitations...

## Slide 4: Challenges in Current PIM Research Tools
Scope Limitations
  Mostly device-centric
  Limited full-system perspective
Technology Support
  Mostly DRAM-centric
  Missing SRAM, STT-MRAM, and other emerging memory technologies
Limited flexibility in architectural modeling
  Assuming naive PE placements and addressing
  Lacking network models for in-memory communication
  Missing proper programming model support
  Missing power models for compute parts

## Slide 5: Our Solution => PIMID
A comprehensive full-system PIM simulator built on proven foundations
  Extended from MultiPIM
  MultiPIM itself is already a somehow mature simulator allowing architectural exploration on PIM
  We exetended it with new capabilities
Key features of PIMID
  Interface to add simulation drivers and models
  Co-simulation of host and PIM devices
  Multiple memory technologies support
  Finer-grained placement of PEs
  Multiple programming model support
  Network model within the memory system
  Power Models for compute and memory

## Slide 6: Key Feature 1: Interface for Extensions
PIMID is based on Intel PIN to generate instruction traces
  Traces are fed to ZSim to for cache simulation and performance counting
  Stats are fed to McPAT for power modelling
  Memory-related instructions are fed to memory simulation models
A standard interface is provided so that
  Additional execution models, memory models and power models can be attached
For simulation drivers, only trace-driven is currently supported, may consider to include execution-driven ones in the future

## Slide 7: Key Feature 2: Host-Device Co-Simulation
Two MultiPIM processes co-simulate at the same time
They communicate through sockets to mimic interactions between host and devices
This enables one run to collect simulation results of the entire system

## Slide 8: Key Feature 3: Multiple Memory Technologies
Current MultiPIM supports DRAM (DDR/HBM) through two extra tools
  Timing from Ramulator
  Power from DRAMPower
PIMID has added timing/power support for
  SRAM through CACTI
  STT-RAM from NVSIM
Simulation parameters are passed to these extra models for the generation of a table having access latencies and energy consumption
An interesting outcome after this would be to allow users to have simulated systems having devices from multiple memory technologies

## Slide 9: Key Feature 4: Fine-Grained PE Placements
PEs in MultiPIM are assumed to have a unified memory address space with the host so PEs can only be seen as rank-level components
  Communication between PEs could only happen through the host memory controller
By allowing the placements of PEs inside memory chips and banks, we need to have Discrete addressing for subarray-/bank-/chip-wide PEs

## Slide 10: Key Feature 5: Multiple Programming Model Support
Programming model support for multi-processing workloads in MultiPIM is shared memory
  Workloads can be written/compiled with OpenMP and run in MultiPIM
  This is OK if PEs are placed in ranks, a directory can be placed in the host MC to guarantee cache coherence between PEs
  However, this is not reasonable if PEs are allowed to be placed near the banks or inside the chips => a lot of coherence traffic is about to cross the host MC
So we added message passing as another option
  Workloads can be written/compiled through MPI with PIMID
  Explicit message exchange happens between the PEs
=> A more realistic option here would be to have
  Memory sharing up to chip scale
    OpenMP-based workloads works if offloaded to PEs in the same chip
  Message passing between PEs communicating beyond memory chips

## Slide 11: Key Feature 6: Flexible Network Support
MultiPIM already has booksim to support networking inside the memory
We integrated GARNET to enable comprehensive network modeling
  Topologies
  Routing algorithms
  Flow control
Can see this as a hypothetic feature since current memory designs only have h-trees and crossbars internally

## Slide 12: Key Feature 7: Comprehensive Power Modeling
No power modelling at all for computing parts in MultiPIM
We added McPAT to support power modelling for the host processor and PEs
  From simple in-order to OoO cores with caches

## Slide 13: Sample evaluation results
32 Banks, 1 in-order PE per Bank
1MB per bank
Woth SRAM, DRAM and STT-MRAM
Tested with BFS workload, message passing
  LHS, execution time, ms
  RHS, energy consumption, mJ
  Bottom, energy break-down for 200K nodes, mJ

## Slide 14: Comparisons with Existing Tools

## Slide 15: Conclusions
PIMID advances PIM research through
  Extensible – More simulation models
  Comprehensive scope - host-device co-simulation
  Technology diversity - DRAM, SRAM, STT-MRAM support
  Architectural flexibility - Fine-grained PE placement with multiple addressing modes
  Programming model for MP workloads - OpenMP + MPI support
  Detailed networking - GARNET-based interconnects
  Complete power modeling - Host, PE, and memory power
Please stay tuned with us for the first release (soon)!

## Slide 16: Back-up slides

## Slide 17: Future Work
Immediate plan
  Open-source release => Community access and contributions
Scheduled updates
  Continued bug fixes and support
  Hardware validation - validation support with FPGA?
  Upgrade to Intel PIN 3

## Slide 18: (Potential) Power of PIM
Assuming each bank has a PE and each PE can directly access the bank
Reality Check
  While PIM offers >10× theoretical bandwidth advantage, real applications typically see 2-10× improvement due to data locality constraints. The true benefit isn't just bandwidth, but massive energy savings by eliminating data movement and enabling highly parallel computations where locality can be maintained.
  Best suited for: Matrix operations, image processing, neural network inference, and database analytics where data can stay local to computation.

## Slide 19: (Potential) Power of PIM (cont.)
Assuming each bank has a PE and each PE can directly access the bank
Limitations
  Data Locality: Data must be in the right bank for processing
  Inter-Bank Communication: Moving data between banks is very expensive
  Load Balancing: Uneven workloads leave many banks idle
  Programming Complexity: Applications need complete restructuring
  Limited Per-Bank Compute: Each PE typically has simple capabilities
  Power & Thermal: 2,048 parallel units create heat challenges
Subarray: 3.3-6.6TB/s
Bank: 820GB/s
Bank Group: 205-410GB/s
Chip: 153.6GB/s
Rank: 153.6GB/s

## Slide 20: Our Solution => PIMID
A comprehensive full-system PIM simulator built on proven foundations
  Extended from MultiPIM
    https://github.com/Systems-ShiftLab/MultiPIM
  MultiPIM itself is already a somehow mature simulator allowing architectural exploration on PIM
  We exetended it with new capabilities
Key features to add
  Co-simulation of host and PIM devices
  Multiple memory technologies support
  Finer-grained configurability
  Network model within the memory system
  Power Model for compute
CPU
MC

## Slide 21: Next Generation High Performance Architecture Research Team RIKEN Center for Computational Science
FugakuNEXT